## Slide 1
ARISS International Delegates Meeting August 20-23, 2015
Report on Post-Commissioning HAMTV reception by single stations and by the European Network of chained ground stations.

## Slide 2
ARISS International Delegates Meeting August 20-23, 2015
ARISS International Delegates Meeting, April 3 - 5, 2014 – ESA ESTEC
An example of HAMTV reception by a single Ground Station equipped with ham-grade hardware: report from Martin, VK6MJ, April 7, 2014
Single station world record

## Slide 3
ARISS International Delegates Meeting August 20-23, 2015
Martin, VK6MJ, station setup
Source: http://www.vivadatv.org

## Slide 4
ARISS International Delegates Meeting August 20-23, 2015
Another example of HAMTV reception by a single Ground Station: F6DZP, op. Jean Pierre, using a “Standard” G/S provided by Kayser Italia on behalf of ESA

## Slide 5
operative
under construction
ARISS International Delegates Meeting August 20-23, 2015
Network of HAMTV chained ground station in Europe (August 2015)

## Slide 6
ARISS International Delegates Meeting August 20-23, 2015
European Network of HAMTV chained ground stations
EIRE National Space Centre, op. EI9FHB Daniel
Poitiers, France, op. F6DZP Jean Pierre
Casale Monferrato, Italy, op. IK1SLD Claudio
Lisboa, Portugal, op. CT2GOY Luis
Kolo, Poland, op. SP3QFE Armand
Matera, Italy, op. ??????? (under construction)
Livorno, Italy, “Test & Back-up” station operated by Kayser Italia
All station are equipped with a 1.2m dish antenna, a Kuhne KU LNC 25 TM Low-Noise-Downconverter and a PROSISTEL Az/El rotator. Periodic check of G/T performances shows the good health of the stations. Hundred of blank-transmissions receptions represented a very useful training of the Network of HAMTV chained ground stations.
Ez/El rotator control-box are currently demanding an upgrade, due to some failure recently reported.

## Slide 7
ARISS International Delegates Meeting August 20-23, 2015
March 20, 2014
One of the first demonstration of chained ground station dislocated in Europe
See on a separate player : HamTV_20_03_2014_8h24UTC.flv

## Slide 8
ARISS International Delegates Meeting August 20-23, 2015
AMSAT Italy developed a MATLAB/Octave computer code, using “Predict” engine (by KD2BD) that allow to create diagrams of monthly occurrences of chained receptions.
Example of chained reception by the 5 European HAMTV G/S. April/May 2014

## Slide 9
ARISS International Delegates Meeting August 20-23, 2015
Well known HAMTV Level Chart, for 1000 km range, baseline configuration.