## Slide 1: Amateur Radio on the International Space Station (ARISS)
ISS Ham: Interoperable Systems
August 2015
ARISS Meeting
http://www.ariss.org

## Slide 2: Agenda
Current situation, including issues and concerns
Potential solutions

## Slide 3: Current Situation
ISS Ham (ISS Program name for ARISS hardware) exists in both segments of the ISS
  Russian Operations Segment (RSOS) Service Module (SM)
  US Operations Segment (USOS) Columbus Module (COL)
Is not easy to move equipment from one segment to the other
  Power: SM is 28 VDC, COL is 120 VDC
    Each uses different connector
  Safety and other certification requirements are different
    What is certified to use in one segment requires re-evaluation of safety and re-certification for the other segment

## Slide 4: Service Module (SM) Status
D700
  Memories non operational due to loss of programming
  Overheats in long key down situations such as cross band repeater operation
  No ability to re-program from the ground
D710
  Essentially an off the shelf D710E with connectors and cable modifications
  Used for school contacts and SSTV
  Memory and parameter programming status unknown
US SSTV Module
  Tends to lockup and stay in transmit mode
  Not currently used
Russian SSTV Module
  Utilizes direct connection to the computer rather than isolated VOX
  Successfully being utilized for Russian SSTV
VCH-1 SSTV system
  Works fine but is limited due to the fact that it needs batteries for power

## Slide 5: D710 in Russian Service Module

## Slide 6: Columbus Module (COL) Status
Ericsson
  Low RF signal on the ground
  Low audio level
  VHF Antenna status after installation is unknown
  UHF module onboard but stowed
DATV System (Ham TV)
  Commissioning of onboard equipment is complete
  In process of completing ground station network
  Little to no crew time for maintenance or testing

## Slide 7: Packet Module and Ericsson Radio in COL

## Slide 8: DATV System in Columbus Module

## Slide 9: Potential path forward – short term (1 of 2)
Develop and deploy a D710 radio in COL with higher power and programmability to replace Ericsson
  Provide identical unit to be used in SM
In order to deploy a D710, a new power supply is required. Develop and provide ARISS-built power supply compatible with ISS Ham components in COL and the Russian Service Module
  Capable of using either 120VDC or 28VDC
  Can use 28VDC from PPS or Russian 28VDC
  Outputs 13.8VDC high power for D710 and USB (5VDC) charging stations
  Deliver two units, one for SM and one for COL
Result would be an interoperable system with components that can be operated in either the Russian SM or the USOS Columbus Module
  Can be moved back and forth in case of on-orbit failure
  Common operations and training

## Slide 10: Possible COL ham station with ARISS LVPS

## Slide 11: Potential path forward – short term (2 of 2)
Develop and deliver Slide Show module which will provide a way to show continuous images in place of the camera (working prototype has shown feasibility)
Upmass or gain access to VSWR/Antenna Analyzer to troubleshoot and understand antenna performance in order to verify proper operation

## Slide 12: Potential path forward – medium term
Develop a controller for the D710 that is based on a personal computing device such as an iPad, Android or other network interface
  Could be used to program the proper memories into the D710 for school contacts ahead of time without crew intervention
  Could possibly be implemented using packet software
  Could be used to provide packet and SSTV capability
    An iPad app from Black Cat Systems already exists

## Slide 13: Potential path forward – long term
Develop common interfaces for power, audio, video and power for all future systemsInteroperabilty across ISS segments
Develop common checkout plans and procedures
Develop common safety packages for all modules on the ISS
Certify all systems for use anywhere on the ISS
A new next generation ham system using a modular approach:
  A core software defined transmitter and receiver
  Separate down converter and up converter modules for each band which are driven by the common software defined transponder
  Antenna switching module
  System programmable and commandable from ground using uplinked files or data streams
  Simple user interface for the crew using uplinked configuration files
  Build upon experience from the system used by ARISSat1 for the transponder
  Allow internal handheld anywhere in the station to communicate to the ground using this transponder

## Slide 14: Summary
Ideas are flowing from across ARISS: Europe, US, Russia with support from Japan
Will require extensive cooperation between Russian and USOS based payload integration and support to allow systems to be used in both segments
Path forward will provide modularity so that system can be continually evolved in pieces as capabilities are desired, available, and funded
  D710 and LVPS are foundational elements for this path forward