## Slide 1: ISS Slide Show Module Overview

## Slide 2: What is it?
  Portable video display module auto sequences still pictures
  Used in place of live Cannon video camera
  Small metal enclosure houses electronics
  Uses Raspberry Pi computer processor (shown below)
  Plugs into existing HamVideo video/power cables
  Uses SD flash card or optional USB drive for video storage
  Pictures can be uploaded from ground via Ethernet port

## Slide 3: Why is it needed?
Replaces blank HamVideo transmissions with actual video
Replaces expensive crew time
Promote Ham interest in school program
Provide means for ground station fine tuning
Encourages Ham ground station construction
Added ground stations help video chaining

## Slide 4: How is it implemented?
Plug module into existing HamVideo video/power cables
Pictures can be uploaded from ground via Ethernet port
Very little crew maintenance time required
Turn on power – unit self loads & starts slide sequence
Unit has internal camera. Press “shutter” button and still picture is captured then added to slide sequence
LED display on front shows picture being processed or crew live video if in “camera” mode.

## Slide 5: Benefits to HamVideo
Easy to build. (I will construct prototype)
Inexpensive. (I will support prototype cost within limits)
Software has been written
Small in size - 7.5” high x 4.5” wide x 2” deep
Can bundle with present upload equipment
Minimum crew maintenance time required
24/7 video for ground station fine tuning
Uses existing video/power connectors & cables

## Slide 6: Equipment Features
Housed in small sealed die cast enclosure
Weight is about 2 pounds
28VDC power is obtained from HamVideo module
28 to 12V / 5v converter for Pi & display within enclosure
“POWER ON” switch and LED located on enclosure front
Slide/camera/shutter switch on enclosure front
Momentary shutter sw. Image captured 10 sec. after actuation
Needed data and power cables presently exist in ISS
Internal camera used for new slides and live video
Internal mike used for live audio or use jack for external mike
Module can be “Velcro” attached to ISS surface
With adapter, audio/video cable compatible with “Raspberry Pi project”

## Slide 7: 1ST prototype internal layout

## Slide 8: Internal Wiring block diagram

## Slide 9: Ham Video Transmitter (video and power connectors at lower front center)