## Slide 1
ARISS International Meeting 2015 – Tokyo, Japan
The Astro-Pi
Ciaran Morgan – M0XTD

## Slide 2: ARISS & the Astro Pi
Summary
What is the Astro – Pi?
How is it being used?
Astro-Pi as a prototype for HAMVideo SlideShow?
Project Selection & Use
Post Principia
Questions

## Slide 3: What is the Astro-Pi?
Based on the Raspberry Pi B+
Includes add-on RTC
Includes SenseHAT
Includes PiCam (normal or NoIR)
Includes additional input buttons
Intended for running school projects during Principia.
Fully functional Pi with all interfaces available.

## Slide 4: What is the Astro-Pi (part II) ?
It is totally encased in a milled aluminium case.
There are two flight models, with another two spare.
ESA Education will be the owner/custodian after Principia

## Slide 5: What is the Astro-Pi (part III) ?
Sensors –
  Humidity
  Temperature
  Pressure
  Gyroscope
  Accelerometer
Will be installed in COLUMBUS
Power provided by AC Invertor and USB plug/charger.

## Slide 7: How is the Astro-Pi being used (Part I)?
Educational Outreach
Designed to allow Tim Peake to interact with school children up and down the UK.
Primary School children (Aged 4-11) were invited to submit ideas for the Pi Foundation to code up – one winning primary school even wrote the code themselves to detect an astronauts presence in COLUMBUS usin the sensor data.
Primary School Expressions of Interest 22 March 2015 Total: 93 (UK: 86)

## Slide 8: How is the Astro-Pi being used (part II)?
Educational Outreach
Designed to allow Tim Peake to interact with school children up and down the UK.
Secondary School children (Aged 11-16/18) were invited to submit fully coded proposals.

## Slide 9: Astro-Pi as a prototype for HAMVideo SlideShow?
Beginnings….
M0XTD met the Pi Educational Partner (Dave Honess M6DNT) and were discussing ideas.
Concept developed out of a help/help situation
  Pi looking for additional uses
  ARISS going to fly SlideShow
Agreed to consider how/where we could collaborate.
…..then developments……
M0XTD aware of issues with the ARISS solution and discussed these with M6DNT
ARISS Project Use and Selection committee held conference call with M6DNT and out of this developed idea of using the Astro Pi as a prototype.
Notes: https://www.raspberrypi.org/blog/astro-pi-mission-update-4/
Each of these programs have been assigned an operational code name that will be used when talking about them over the space to ground radio.
Ops name: FLAGS
School: Thirsk School
Team name: Space-Byrds
Key stage: 3
Teacher: Dan Aldred
The judges had a lot of fun with this. Their program uses telemetry data provided by NORAD along with the Real Time Clock on the Astro Pi to computationally predict the location of the ISS (so it doesn’t need to be online). It then works out what country’s territory the ISS is above, and shows its flag on the LED matrix, along with a short phrase in the local language.
Ops name: MISSION CONTROL
School: Cottenham Village College
Team name: Kieran Wand
Key stage: 3
Teacher: Christopher Butcher
Kieran’s program is an environmental system monitor that could be used to cross check the ISS’s own life support system. It continually measures the temperature, pressure and humidity, and displays these in a cycling, split-screen display. It has the ability to raise alarms if these measurements move outside of acceptable parameters. We were especially impressed that code had been written to compensate for thermal transfer between the Pi CPU and Astro Pi sensors.
Andy Powell of the Knowledge Transfer Network said:
“All of the judges were impressed by the quality of work and the effort that had gone into the winning KS3 projects and they produced useful, well thought through and entertaining results”
Ops name: TREES
School: Westminster School
Team name: EnviroPi
Key stage: 4 (and equivalent)
Teacher: Sam Page
This entry will be run in the cupola module of the ISS with the Astro Pi NoIR camera pointing out of the window. The aim is to take pictures of the ground and to later analyse them using false colour image processing. This will produce a Normalised Differentiated Vegetation Index (NDVI) for each image which is a measure of plant health. They have one piece of code which will run on the ISS to capture the images and another that will run on the ground after the mission to post process and analyse the images captured. They even tested their code by going up in a light aircraft to take pictures of the ground!
Ops name: REACTION GAMES
School: Lincoln UTC
Team name: Team Terminal
Key stage: 4 (and equivalent)
Teacher: Mark Hall
These students have made a whole suite of reaction games, complete with a nice little menu system to let the user select them. The games also record response times, with the eventual goal being to investigate how crew reaction time changes over the course of a long-term space flight. This entry caused all work to cease during the judging for about half an hour!
Lincoln UTC have also won the prize for the best overall submission in the Secondary School completion. This earns them a photograph of their school taken from space by an Airbus or SSTL satellite. Go and make a giant space invader please!
Ops name: RADIATION
School: Magdalen College School
Team name: Arthur, Alexander and Kiran
Key stage: 5 (and equivalent)
Teacher: Dr Jesse Petersen
This team have successfully made a radiation detector using the Raspberry Pi camera module, the possibility of which was hinted at during our Astro Pi animation video from a few months ago. The camera lens is blanked off to prevent light from getting in, but this still allows high-energy space radiation to get through. Due to the design of the camera, the sensor sees the impacts of these particles as tiny specks of light. The code then uses OpenCV to measure the intensity of these specks and produces an overall measurement of the level of radiation happening.
What blew us away was that they had taken their Astro Pi and camera module along to the Rutherford Appleton Laboratory and fired a neutron cannon at it to test it was working!
The code can even compensate for dead pixels in the camera sensor. I am wondering if they killed some pixels with the neutron cannon, and then had to add that code out of necessity? Brilliant.
These winning programs will be joined on the ISS by the winners of the Primary School Competition which closed in April:
Ops name: MINECRAFT
School: Cumnor House Girl’s School
Team name: Hannah Belshaw
Key stage: 2
Teacher: Peter Kelly
Hannah’s entry logs data from the Astro Pi sensors, and visualises it later using structures in a Minecraft world. So columns of blocks are used to represent environmental measurements, and a giant blocky model of the ISS itself (that moves) is used to represent movement and orientation. The code was written, under Hannah’s guidance, by Martin O’Hanlon who runs Stuff About Code. The data logging program that will run on the ISS produces a CSV file that can be consumed later by the visualisation code to play back what happened when Tim Peake was running it in space. The code is already online here.
Ops name: SWEATY ASTRONAUT
School: Cranmere Primary School
Team name: Cranmere Code Club
Key stage: 2
Teacher: Richard Hayler
Although they were entitled to have their entry coded by us at Raspberry Pi, the kids of the Cranmere Code Club are collectively writing their program themselves. The aim is to try and detect the presence of a crew member by monitoring the environmental sensors of the Astro Pi, particularly humidity. If a fluctuation is detected it will scroll a message asking if someone is there. They even made a Lego replica of the Astro Pi flight case for their testing!
Obviously, the main prize for winners is to have your code flown into space and run on the ISS. However, the UK Space companies also offered a number of thematic prizes which were awarded independently of those that have been chosen to fly. Some cross-over with the other winners was expected here.
Space Sensors Hannah Belshaw, from Cumnor House Girl’s School with her idea for Minecraft data visualisation.
Space Measurements Kieran Wand from Cottenham Village College for his ISS environment monitoring system.
Imaging and Remote Sensing The EnviroPi team from Westminster School with their experiment to measure plant health from space using NDVI images.
Space Radiation Magdalen College, Oxford with their space radiation detector.
Data Fusion Nicole Ashworth, from Reading, for her weather reporting system; comparing historical weather data from the UK with the environment on the ISS.
Coding Excellence Sarah and Charlie Maclean for their multiplayer Labyrinth game.
Pat Norris of CGI said:
“It has been great to see so many schools getting involved in coding and we hope that this competition has inspired the next generation to take up coding, space systems or any of the many other opportunities the UK space sector offers. We were particularly impressed by the way Charlie structured his code, added explanatory comments and used best practice in developing the functionality.”
We’re aiming to have all the code that was submitted to the competition on one of the ten SD cards that will fly. So your code will still fly even if it won’t be scheduled to be run in space. The hope is that, during periods of downtime, Tim may have a look through some of the other entries and run them manually. But this depends on a lot of factors outside our control, and so we can’t promise anything.
But wait, there’s more!
There is still opportunity for all schools to get involved with Astro Pi!
There will be an on-orbit activity during the mission (probably in January or February) that you can all do at the same time as Tim. After the winning programs have all finished, the Astro Pi will enter a phase of flight data recording. Just like the black box on an aircraft.
This will make the Astro Pi continually record everything from all its sensors and save the data into a file that you can get! If you set your Astro Pi up in the same way (the software will be provided by us) then you can compare Tim’s measurements taken in space with yours taken on the ground.
There is then a lot of educational value in looking at the differences and understanding why they occur. For instance, you could look at the accelerometer data to find out when ISS reboosts occurred; or study the magnetometer data to find out how the Earth’s magnetic field changes as they orbit the Earth. A number of free educational resources will be provided that will help you to leverage the value of this exercise.
The general public can also get involved when the Sense HAT goes on general sale in a few weeks time.
Libby Jackson of the UK Space Agency said:
“Although the competition is over, the really exciting part of the project is just beginning. All of the winning entries will get to see their code run in space and thousands more can take part in real life space experiments through the Flight Data phase”

## Slide 10: Astro-Pi as a prototype for HAMVideo SlideShow?
Issues identified by ARISS
Originally proposed Pi Model B
Capacitors required replacement
Connectors required replacement?
Connection to HAMVideo unit via dedicated cable?
On power failure, serious risk of microSD card corruption.
Pi Interrupts did not work when used headless
Issues identified by Rasbperry Pi
Model B deprecated
Cannot purchase AstroPi
Only available to schools
MicroSD card corruption – UK flying 10 spare SD cards in case of problem
No ISS network access
No facility to take data/results of the Pi other than at end of mission when SD card returned to earth……..
Etc etc etc
*tbd in talk on “Raspberry Pi”

## Slide 11: Astro-Pi as a prototype for HAMVideo SlideShow?
Resources on Astro-Pi
Websites
Educational Resources
  R-Pi Foundation
  Python.org
  etc
M0XTD decided to build one

## Slide 12: Astro-Pi as a prototype for HAMVideo SlideShow?
M0XTD-Pi
Capabilities
Based on Raspberry Pi B+
Using Kernel 4.0.9+
Astro-Pi software installed.
GPS/PPS clock instead of RTC
Two additional tactile buttons added (mirrors Btn A and B on Astro-Pi)
Uses 4-pole connector for composite video

## Slide 13: Astro-Pi as a prototype for HAMVideo SlideShow?
Can take MoXTD-Pi microSD card and place it in AstroPi unit and receive identical behaviour.
Can run the existing ARISS SlideShow software
Solved problem of interrupts
Identified solution to microSD Card corruption issue.
Interface cable between Pi and HAMVideo simplified

## Slide 14: Astro-Pi as a prototype for HAMVideo SlideShow?
Existing
Existing
Proposed

## Slide 15: Project Selection & Use
Proposal to PS&U to continue to develop the solutions to the existing problems, foster and build the right relationships to allow R-Pi Foundation and ARISS to partner together and seek agreement to use Astro-Pi as a prototype for the SlideShow.
Conditional acceptance given with requirements, all of which are capable of being delivered.
Notes: Ciaran -
Yes, the request for documentation is for whatever would be used by ARISS. However we can get them would be helpful.
For the new images/SW we were mostly intending to start the discussion so we don’t necessarily expect answers right away. However, I imagine that an 8 GB upload would be difficult, either to a PC or via the network, but I don’t really know. We’ll have to keep thinking about this one.
Can the card be set up such that the image files are in a separate folder and are the only things that would need to be changed, exclusive of a software update? That would make the bulk of the changes easier to accomplish onboard: just put in the MicroSD card and update the photo files.
BTW, I think a MicroSD adapter would be necessary. Any idea how that is being handled?
A full software update will need to be worked out, but that is farther down the road.
See you soon.
Thanks!
Mark
From: Ciaran Morgan <ciaran.morgan@rsgb.org.uk> Date: Thursday, August 6, 2015 at 5:12 PM To: Mark Steiner <Mark.Steiner@nasa.gov> Cc: Lou McFadin <arissw5did@comcast.net>, Frank Bauer <ka3hdo@verizon.net>, Oliver Amend <oliver.amend@ohb-system.de>, Oliver Amend <oliver.amend@gmx.de>, Rosalie White <rwhite@arrl.org>, Kenneth Ransom <kenneth.g.ransom@nasa.gov> Subject: RE: Request from the PSU Committee for further information
Hello Mark,
Thank you for the feedback and the recommendation.
I don’t believe that any of the questions asked will be problematic to answer and I am working on the answers as we speak.
I have also raised some questions, and had a brief discussion on the call tonight that will help answer the power question.
On the full disclosure question – is this aimed at the AstroPi unit, what is inside it and how it is connected within the station? If so, I am aware that these documents exist as part of the flight approval for the AstroPi and that the R-Pi Foundation/ESA Education have them. The R-Pi Foundation cannot release them to me but I do know who to speak to in ESA Education if that is what is needed.
The new images/software is an interesting question. In the absence of a network connection to the Pi, my understanding was that all that was possible was to up mass a micro SD card specifically for the purpose – i.e that we have a set of static images and/or videos and that to change them, we had to up mass a new card (or get the network connection approved). If I read your question correctly, are you saying that NASA has a file transfer capability to the station and on board the station can create images on SD/micro SD cards in orbit? If this is the case, can this system handle the upload of a minimum file image of 8GB? I am completely ignorant of this side of the stations/NASA operations and would need some help to come up with a workable plan if this was indeed to be the route that is used for the upload.
I hope to have as many answers as I can next week and will update the proposal accordingly.
As an aside, some engineering modules of the AstroPi have been made available to the Principia Outreach partners and I am trying to get hold of one of them to take to Japan alongside the “pseudo-AstroPi” unit that I have built to test out my ideas. Hopefully that will help resolve the problems so that we can produce a functional software build specification which I am also guessing is another deliverable I will have to add to the list!!
Looking forward to meeting you and everyone else in Japan in a couple of weeks.
73
Ciaran – M0XTD
From: Steiner, Mark D. (GSFC-5990) [mailto:mark.steiner@nasa.gov] Sent: Wednesday, August 05, 2015 9:45 PM To: Ciaran Morgan <ciaran.morgan@rsgb.org.uk> Cc: Lou McFadin <arissw5did@comcast.net>; pdcowan@rogers.com; c.avmdti@free.fr; Samburov Sergey Nikolaevich (Russia-RSCE) <Sergey.Samburov@rsce.nasa.ru>; Sergey Samburov <RV3DR@mail.ru>; tsuruday@gmail.com; Frank Bauer <ka3hdo@verizon.net>; Oliver Amend <oliver.amend@ohb-system.de>; Oliver Amend <oliver.amend@gmx.de>; Rosalie White <rwhite@arrl.org> Subject: Request from the PSU Committee for further information
Ciaran -
The ARISS PSU met today and discussed your AstroPi proposal. Here is a summary of our discussions:
Just today we updated the submission guidelines to include a requirement for full disclosure of technical documentation. It is paragraph 8.7 in the attached new guidelines. Will this be an issue?
Lou would like to know how it is powered.
We need to have you provide a block diagram of the Astro Pi system, particularly how it is to be connected to other ARISS hardware.
How will new images and software be transferred to unit onboard? From ground computer to onboard network? MicroSD card image uploaded to NASA computer and then put on MicroSD card for physical installation?
The Committee’s recommendation to the ARISS delegates is for conditional approval, pending resolution of the above questions and requests.
Please let us know how soon you think you could provide the above information. Once we receive your updated proposal we will share it with the PSU Committee for either final approval or request for more discussion, and we’d like to have this wrapped up prior to the ARISS-I meeting in Japan.
Thank you. Please let me know if you have any questions.
Mark Steiner, K3MS
NASA ARISS Technical Liaison
NASA-GSFC/Code 599
Greenbelt, MD 20771
Office - 301-286-4285 Cell - 301-502-0983
*************************************************

## Slide 16: Post Principia
What happens next?
Ownership/Custodian transfers to ESA Education from UKSA
Will be used for future education outreach
Raspberry Pi Foundation still involved
Procedures need to be worked up to manage the use of the Astro Pi units.
Also need to figure out how data can be sent/retrieved from Astro-Pi – is there an opportunity to include the Amateur Radio communication facility as part of this?

## Slide 17: Questions?