## Slide 1: Ham Video On-orbit Functional Commissioning - B.USOC Contribution
ARISS Workshop
3 – 5 April 2014
ESTEC

## Slide 2: Outline
Few words about B.USOC
Operations of Ham Video Commissioning
  Set-up
  Execution
B.USOC involvement after Commissioning

## Slide 3: B.USOC in few words…
Belgian User Support and Operations Centre is located in Brussels, Belgium.
The B.USOC was created in 1997 by the Belgian Science Policy within the framework of the European Space Agency ISS Exploitation program.
The centre supplies to scientists or end users a set of services and resources to prepare, perform, monitor and analyse experiments on board a facility on the ISS or other satellite platforms.

## Slide 5: B.USOC recent missions

## Slide 6
PCDF (Protein Crystallization Diagnostics Facility)
March 2009 – July 2009
15A (STS-119)
2J/A (STS-127)
In-situ observation of nucleation and crystal growth behavior of protein crystallization in microgravity.
To achieve experimental and operational flexibility, extensive preparation was needed.
24/7 console coverage.

## Slide 7
SOLAR: February 2008 – today

## Slide 8: METERON (2012- 2014)
Teleoperation tests of a robot on the ground from the ISS using DTN to simulate aspects of exploration missions

## Slide 9: Ham Video Commissioning: The Set-up

## Slide 10: Ham Video front panel
COL antenna
(transmission)
PPS
(Power)
Camera
(image data)
HAM Video
Power ON/OFF
8 configurations
Transmission
Power ON/OFF

## Slide 11
Configurations cue card

## Slide 12: Ham Video and HW used for the commissioning:
ESA Portable Pwr Supply (KUPS) (available in Columbus)
ARISS 2 S/L-Band COL Antennas (mounted outside Columbus Module)
Ham Video hardware (uploaded with HTV-4)
Canon XF-305 with 1 flash card dedicated to Ham Video (provided by NASA via PIA agreement)
Multiuse Bracket Assembly dedicated to Ham Video (provided by NASA via PIA agreement)
Canon BP-955 fully charged batteries from ISS pool (provided by NASA: will be requested in via CEF, also mentioned in PIA)

## Slide 13
The on-orbit accommodation in Columbus:
HAM VIDEO on D1 rack, in front of ER#3
Canon XF-305 Camera on EDR left rack seat track (mounted with bogen arm and used on batteries only)
Portable Pwr Supply (KuPS) on D2 rack for PPS activation: PDU 2 outlet 11

## Slide 14: Flight and Ground Segment operations set-up:

## Slide 15: Crew Training & Simulations

## Slide 16: Commissioning status
Installation
Pass 1:
Config.Test
Antenna #41
Blank Transmission
Pass 2:
Config.Test
Antenna #43
Blank Transmission
Pass 3:
Config.Test #41 or #43
(reserve)
Blank Transmission
Legend:
Blue box: Crew activity
Green Box: Gnd activity
Dark blue frame: time critical
Performed March 6, 2014, by R. Mastracchio
March 8, 2014
by M. Hopkins
March 9 2014
by M. Hopkins
Not used
Pass 4:
Functional Test

## Slide 17: Commissioning status:
Installation
Pass 1:
Config.Test
Antenna #41
Blank Transmission
Pass 2:
Config.Test
Antenna #43
Blank Transmission
Pass 3:
Config.Test #41 or #43
(reserve)
Blank Transmission
Pass 4:
Functional Test
Legend:
Blue box: Crew activity
Green Box: Gnd activity
Dark blue frame: time critical
NET 12 April by K. Wakata (TBD)

## Slide 18: Pass 4
NET 12 April (TBD)
No Ham Video activities during SpaceX-3 docked timeframe.
Only trained crew is K. Wakata, coming back on 13 May.
After Pass-4 Ham Video is switched off, the bogen arm and the camera will be stowed and the hardware ownership will be handed over to ARISS/NASA.

## Slide 19: After Commissioning…
B.USOC will create a generic PODF to handle Ham Video (pwr on and configuration change)
All ops products will be handed over to ARISS/NASA (POC?)
Support required for the planning?

## Slide 20: ESA PODF’s
PODF TITLE | Status
1.100 Ham Video Installation | All ready in IPV
1.200 Ham Video Deinstallation | 
1.300 Ham Video Commissioning | 
3.100 Ham Video Yellow LED Contingency Operations | 
3.200 Ham Video Green LED Contingency Operations | 
9.001 Ham Video Cue Card | 

## Slide 21: B.USOC Lessons Learned
Technical assessments of transmitter interferences with systems from other International Partners and Flight Rule discussions have unfortunately delayed the commissioning significantly
Several simulations organized together with ARISS and Col FCT highly contributed to smooth and efficient execution of the passes.
Briefing with ARISS pre and post the pass.

## Slide 22
Thank you!
ham-video@busoc.be