## Slide 1: HamTV, a practical approach
ARISS ESTEC meeting 3-5 April 2014

## Slide 2: HamTV, a new challenge
HamTV that is now ready for sending video and audio, give us new possibilities for ARISS school contact but is also a new challenge for HamRadio that will have to overcome specific technologies :
    Use of high gain antenna: dish or several helix…
    Use of LNA or down converter
    Struggle against interferences
    Setup of tracking equipment and software
    Acquire basic knowledge of DVB technology
    Use of Software for receiving, decoding and streaming
    Use of recorded data.

## Slide 3: With TT S2-3200 or TT s2-1600 PCI card, several software
  Tiny Spectrum Analyzer (TSA), that can analyze your LNB/LNA gain, interferences, global noise level…
  Noise Power Measurement (NPM) that will help us to set the tracking system by measuring the sun noise.
  Tutioune1600 or 3200 that will analyze the signal and extract the TS (Transport Stream), decode it or send it to other software for decoding, analyzing…
  TiouneData Reader that will give us the best report we could have about signal, RF level, S/N..

## Slide 4: TinySpectrum Analyzer S2-1600
Full scan:
we scan from 600 MHz to 2600 MHz.
This is the Kuhne KN23 output with a dummy load.
We can see the 916 500 LO freq (and 1 833 000).
As it is a down converter we will see 2.422GHz with S2-1600 tuner set to 2422000 – 916500 = 1 505 500 kHz

## Slide 5: TinySpectrum Analyzer S2-1600
Watching 2422 MHz
Scan width 500 MHz, we principaly see the LNB amplification in the middle on the band, centered around 2400 MHz.
We must set a lower bandwidth and put an antenna

## Slide 6: Scan width 125 MHz + little wifi antenna

## Slide 7: Scanwidth 65 MHz with little wifi antenna

## Slide 8: Scanwidth 65 MHz with little wifi antenna after 5 mn …

## Slide 9: Scanwidth 65 MHz with external dish

## Slide 10: Scanwidth 65 MHz with external dish +5mn

## Slide 11: 2437 MHz !!!

## Slide 12: 2395 MHz after 5 mn

## Slide 13: Chinese down converter 2422 MHz and 24 dB attenuation

## Slide 14: Chinese Down conv. After 5 mn

## Slide 15: Using NPM tracking the sun

## Slide 16: dBm

## Slide 17: Tutioune (“2-Tune”)
RECEIVING AND MEASURING
DVB-S SIGNALS

## Slide 18: Commercial Example: PCI Tuner TT S2-3200

## Slide 19: TT S2-3200 Internals
L-Band receiver
Wide band, phase modulated signal
STB6100 processes RF signal
Analogue differential I and Q signals
QPSK demodulator, STB0899, Processes I and Q signals
Transport Stream is transferred to the PC via the Multimedia processing chip, SAA7146a , connected to the PCI bus of the PC.
The software sends instructions to setup STB0899 via a I2C. The instructions are sent to the STB6100 synthesizer via an I2C repeater.

## Slide 20: STB6100 Block Diagram
Tuning steps = 27 MHz/1024 = 26.367 kHz.
VCO frequency controlled by STB0899 via I2C
Bandwidth 5-36 MHz
Baseband gain (-10 dB to +14 dB)
AGC controlled by STB0899
AGC range = 70dB typical
Baseband gain = 17dB max
Dynamic range = 87dB. 2 Analogue I/Q signals at the RF frequency, corresponding to the selected symbol rate. Feed into QPSK demodulator

## Slide 21: STB0899 DVB-S Demodulator
I/Q signals are immediately digitised at 108 MHz
All digital processing thereafter, inc. multiple PLL, Nyquist filters, equalisation.
STB0899 Functions In Order:
Digitising I and Q, Integration of signals to calculate AGC1 Locking RF frequency
Locking Symbol Rate frequency
Equalisation to suppress echoes in coaxial cable, De-mapping, Viterbi decoding
De-interlacing, Reed Solomon decoding, Removing energy dispersion coding
Obtaining TS Stream (detection of header bytes, packets…)

## Slide 22: Measuring DVB-S Signal From RF to Video
Initially there are video and audio signals that have been digitised and multiplexed to give a series of digital values, consisting of bits (0 or 1): 0010101110101101101 .... The principle of a DVB-S transmission is to continuously send (for QPSK modulation of a carrier) "Symbol" called IQ, which can be regarded as the coordinates (I, Q) of a point and which, as the dial is the point wherein, means 00, 01, 10 or 11.
With these Symbols received, we will reconstruct the byte stream of information that has been digitised and transmitted after a whole process to correct the errors and re-order the video, audio, etc ... We can already see that the constellation (drawing representing four quadrants and IQ points) will help us to see if the points are well placed and if it is easy to determine what combination (00 or 01 or 10 or 11) they represent. Faults in transmission and reception, will lead to a greater or lesser dispersion of these points, as we will see later.

## Slide 23: Measuring Signal Levels
RF level
This is the standard measurement use in amateur radio, it can be represented in these ways:
  S point
  dBμ Volt
  dBm
  or more recently by LED segment displays.
Spectrum analyser (SEFRAM7856)
Not every OM has one in his shack
I and Q levels
  IQ signals supplied by the ZeroTuner have an amplitude of 0 to 1 Vpp, generally (or 0 to 2 Vpp for the STB0899 demodulator)
  Frequency of the order of a few MHz
  The small Tutioune oscilloscope displays these signals 

## Slide 24: Measuring Signal to Noise
There are 5 main Signal to Noise measurements in common use:
  CNR (RF)
  Analogue SNR (analogue IQ)
  Digital SNR (digital IQ)
  MER
  EVM

## Slide 25: Measuring Signal to Noise… CNR
CNR or C/N
  Well known in Ham Radio, used with analogue RF signals, this is the Carrier to Noise Ratio, the ratio between the signal and the noise
  The CNR is used by analogue TV operators, measured using spectrum analysers (in dB)
  Not accurate to state that "the greater the CNR, the greater the ability to decode the digital stream without errors”
  It is possible to have CNR of 30 dB with a "beautiful" castle shape on a spectrum analyser but not have a usable video stream to decode
  Conclusion: CNR gives you little DATV information, except if it is very low or almost zero.
CNR = value in dB (Y-axis) between the upper triangle and the lower blue square / cross
.

## Slide 26
Analogue SNR (Analogue IQ) or S/N
Signal to Noise Ratio, Signal / Noise, the ratio between the signal of interest and noise.
Signal is called Baseband and corresponds to two signals I and Q modulated in phase at a frequency depending on the symbol rate.
The SNR is determined by the same kind of measurements as for the CNR but using IQ. The signal amplitude is 0 to 1 or 2 Vpp therefore a level that has nothing to do with the RF signal and on lower frequencies (several MHz). The minimum SNR at the input of QPSK demodulator must be at least 1dB for it to be able to Timing sync lock (doc STMicroelectronics).
In general we don’t have easily access to these signals (analogue IQ)
Measuring Signal to Noise… Analogue SNR

## Slide 27
Digital SNR (Digital IQ)
In the circuit where I and Q are digitised at about 100 MHz, 6 bits mostly but 8 bits for STB0899 demodulator. The Effective Number of Bits (ENOB)* is 7.5 bits. This gives a possibility 45 dB dynamic range if the entire scanning was used.
The digital SNR can be the theoretical maximum of 45dB but if you look at the range of values taken by IQ seen in practice, it remains to lower values. Consequences of ENOB n: Dynamic Range DR = maximum digital SNR= 20log10 (2n) dB (n being the number of bits used for coding) or easier to remember: SNR Max = 6.02 x n (dB)
So, if we use 16-bit coding, we get a maximum ratio of 96.3 dB,( this is how we can say that the theoretical maximum dynamic recording an audio CD is 96 dB.) So here SNRmaximum depends of number of bits on which we code I and Q. If I and Q are coded on 8 bits (STB0899 case) there is a dynamic theoretical maximum of 48 dB, but it quickly becomes clear that the amplitude of the digitized values of IQ does not occupy the entire range possible. The SNRmax depends on the ENOB (Effective Number of Bits)
* The ENOB used in the calculations of SNR is a case where a number of bits is strangely not always an integer, so, it must therefore be considered more as a calculation coefficient.
Measuring Signal to Noise… Digital SNR

## Slide 28
Modulation Error Ratio (MER) using digital IQ
MER is often the primary measurement of the quality of a DVB signal. Virtually all DVB analysers place priority on MER (Eg. DMA120 Analyzer Tektronix)
MER on an SEFRAM analyser:
MER on Tutioune:
Measurements made with an RF level (-36 dBm) and high CNR almost constant.
There are 2 displays for MER and constellations, as they are interrelated.
Measuring Signal to Noise… MER

## Slide 29: MER
MER (Modulation Error Ratio), it is a method of measuring the SNR Digital (MER depends on a whole range of defects on the IQ signal, SNR num, phase noise, jitter, but with DVB-S, digital SNR is the main default). The MER is a measure of the quality of the modulation. (Source: Hewlett-Packard)
From this graph, we can do 2 kinds of calculations:
- based on knowledge of the importance of this error vector (it will calculate the EVM)
- based on a calculation of the average / cloud will be the MER
MER is a good measurement because it is in dB and is easily represented in our minds by recalling the constellation
My own opinion: MER should become the key measure for giving a report in DATV, summarising the main characteristics of the signal and the difficulties to decode or not the received signal.
Measuring Signal to Noise… MER cont.

## Slide 30: Measuring Digital Stream Error Rate
Tutioune presents these values in this form:
Tutioune gives VBER% with the no. of bits corrected by Viterbi x msec (between 2 readings) and the number of bits corrected by Reed Solomon.
CBER: Error rate before Viterbi
correction
VBER: Error rate after Viterbi correction
UNC packet error rate: ratio of number of wrong packets / number of packets
transmitted during the measurement time.

## Slide 31: Transport Stream Measurements
Information on rates, errors (CRC) And PIDs table structure
“TS Reader”

## Slide 32: Transport Stream Measurements
“Video Analyzer”

## Slide 33: Measuring the Quality of Video Encoding
Within DATV transmissions, everything is contained as a digital stream, the video does not exist in an analogue form. Decoded video can be displayed directly on a digital LCD display via HDMI/DVI
Any measurement such as S / N video, on a video signal that now exists only in the form of bytes, would be nonsense
There are tools to analyse the encoding efficiency of MPEG-2 or H.264
This specialised software is capable of analysing the output of MPEG-2/H.264 encoders and audio encoders and multiplexers
But we do not enough time to explore this subject today…

## Slide 34: When a signal is good?
When discussing DATV reception, we are often asked the question: “What are the best values for RX?”
  An RF level of -50dBm?
  15dB SNR?
  An MER of 14dB?
The answer is that none of these parameters may be sufficient to guarantee that the reception will be OK.
It is more important to be able to determine that the signal cannot be improved further.
Observing the MER and VBER and no. of bits corrected by Viterbi and Reed Solomon, tells me when I am at the limit of the capabilities of the demodulator.
Simple observation, of the TS LED on the Tutioune instrument panel tells us:
  Green = “stream OK”
  Red = “no stream”
  Look at next page to observe that the RF level remains the same, CNR remains the same, but the MER goes down (I added phase noise to the modulation)

## Slide 35
MER 18dB -----RF level -36dBm ----VBER 0% not bit corrected TS OK
MER 5.8dB -----RF level -36dBm ----VBER 4% bits corrected by Viterbi TS OK
MER 4dB -----RF level -36dBm ----VBER 18% bits corrected by Viterbi and Reed Solomon TS OK
MER 2.7dB -----RF level -36dBm ----34% bits corrected by Viterbi and Reed Solomon TS NOT OK
DATV Analysis Examples

## Slide 36: Tutioune

## Slide 37: Tutioune: Basic Mode
Check Frequency Lock
Check SR Lock
RF Signal level display in dBm
MER displayed in dB
Constellation display
FEC discovered, VBER indication in %, No. of bits corrected by the Viterbi corrector, No. of bits corrected by Reed Solomon corrector
TS LED Green = all okay
Channel LED indicates that software DMA access to PCI Bus
OUT LED flashes corresponding to good packets received and SR rate
Beep button generates audio tone that rises with MER (antenna alignment)
Expert mode for IQ signal, BaseBand gain…

## Slide 38: Tutioune: Expert Mode Interface

## Slide 39: TiouneMonitor: Web Monitoring
Red icon = Offline OM with Tutioune + Web Monitoring
Green icon = Online OM with Tutioune + Web Monitoring.
Green bouncing icon = OM with Tutioune + Web Monitoring with live DATV RX

## Slide 40: TiouneMonitor
Monitor your own transmissions as received remotely.
A unique and powerful tool. The most accurate way to give true, real time, signal reports.

## Slide 41: TiouneData Reader and HamTV reports

## Slide 42: Chaining Ground Stations

## Slide 43: 3 TiouneData

## Slide 44: Result of chaining

## Slide 45: Future developments, wishes...
All software can be found on :
www.vivadatv.org

## Slide 46: Conclusion
Thank you for your attention