## Slide 1: Amateur Radio on the International Space Station (ARISS)
ISS Ham Equipment:
Status and Plans
April 3, 2014
http://www.ariss.org

## Slide 2: Agenda
Current situation, including issues and concerns
Long-term strategic planning and potential solutions

## Slide 3: Current Situation
ISS Ham (ISS Program name for ARISS hardware) exists in both segments of the ISS:
  Russian Operations Segment (RSOS) Service Module (SM)
  US Operations Segment (USOS) Columbus Module (COL)
Is not easy to move equipment from one segment to the other:
  Power: SM is 28 VDC, COL is 120 VDC
    Each uses different connector
  Safety and other certification requirements are different
    What is certified to use in one segment requires re-evaluation of safety and re-certification for the other segment

## Slide 4: Service Module (SM) Status
D700
  Memories non operational due to inadvertent improper programming.
  Overheats in long key down situations such as cross band repeater operation.
  No ability to re program from the ground.
D710
  Very little known about this unit’s modifications and potential uses.
  No microphone onboard until recently.
SSTV Module
  Tends to lockup and stay in transmit mode.
  Difficult to trouble shoot due to multiple possibilities of problem cause.
VCH-1 SSTV system
  Works fine but is limited due to the fact that it needs batteries for power.
Little to no crew time for maintenance or testing.

## Slide 5: Columbus Module (COL) Status
Ericsson
  Low RF signal on the ground.
  Low audio level
  VHF Antenna status after installation is unknown
  UHF module onboard but stowed
DATV System (Ham TV)
  Recently delivered onboard
  Commissioning in process
  Still requires VHF audio uplink during extended DATV session
Little to no crew time for maintenance or testing.

## Slide 6: Potential Solutions (1 of 3)
Ericsson low RF signal (COL)
  Add power amplifier to increase the signal to at least 15 watts or replace with higher power radio such as the D710
  Develop and provide power supply compatible with ISS Ham components in COL
  Make necessary modifications to get through safety review
    Add a fan
    Develop a way to re-program while onboard ISS
  Upmass or access VSWR meter to assist in verifying proper operation and troubleshooting
Ericsson low audio (COL)
  Modify the adapter module to increase the mic. gain
  Crew be trained to “eat” the microphone
  Replace radio with a new unit that has a different type microphone such as the D700 or D710

## Slide 7: Potential Solutions (2 of 3)
D700 (SM)
  Replace with new radio or reprogram D700 on-orbit
D710 (SM)
  Upmass microphone
  Reprogram D710 to support voice ops

## Slide 8: Potential Solutions (3 of 3)
SSTV Module
  Modify to allow adjustment of the audio threshold and hysteresis
  Consider use of USB port instead of computer microphone to reduce interference effects
DATV System
  Find a way to provide a camera that does not use batteries
  Provide a way to use a memory stick or SD card to provide a video or slide show when a camera is not available
  Add a beacon module which incorporates a power supply for the D710 (COL) and provides slide show and other capabilities

## Slide 9: Potential path forward – short term
Develop and deploy a D710 radio in COL with higher power and programmability
In order to deploy a D710, a new power supply is required:
  Option 1: work with Kaiser Italia and ESA to develop the S-Band Beacon module as defined by the requirements document already developed which has power supplies for D710 and VC-H1
  Option 2: Develop an ARISS built power supply or S-Band beacon module as defined by the requirements document already developed
Upmass or access VSWR/Antenna Analyzer to understand antenna performance

## Slide 10: Possible CM ham station with Beacon/Transponder

## Slide 11: Joint ARISS/Kaiser Italia S Band Beacon

## Slide 12: KI Proposal

## Slide 13: Potential path forward – medium term
Develop a controller for the COL & SM D710 based on a personal computing device such as an iPad or Android
  Could be used to program the proper memories into the D710 for school contacts ahead of time without crew intervention
  This could be implemented using packet software
  Could be used to provide packet and SSTV capability. There is already an app for that on the iPad from Black Cat Systems.

## Slide 14: Potential path forward – long term
Develop common interfaces for power, audio, video and data for all future systems  Interoperabilty across ISS segments
Develop common checkout plans and procedures
Develop common safety packages for all modules on the ISS
Certify all systems for use anywhere on the ISS
A new ham system using a modular approach:
  A core software-defined transmitter and receiver, allowing for new modes
  Separate down converter and upconverter modules for each band which are driven by the common software-defined transponder
  Antenna switching module
  System programmable and commandable from ground using uplinked files or data streams
  Simple user interface for the crew using uplinked configuration files
  Adapt the system built for ARISSat for the transponder
  Allow internal handheld anywhere in the station to communicate to the ground using this transponder (Bluetooth? WiFi? low-power RF link?)
Identify educational benefits as part of package to obtain funding