## Slide 1
Webcast strategy
for ARISS events
Gianpietro Ferrario – IZ2GOJ

## Slide 2
Introduction
Transmitting live an ARISS school contact, using a simple webcam, would help sharing the event with people and students everywhere in the world.
Goals:
Involving in the school the largest amount of students, even if in the event room they’re not able to host all of them in person
Involve other schools/students from far away
Spreading the ARISS project awareness maximally
Useful for HAM radio groups potentially interested in the ARISS project but not informed on how to conduct en event
Advantages:
No need for a dedicated PC
Plug and play, just connect camera, network and audio plugs
Very easy and cheap configuration (less than € 100)
We could share the software installation package, to be easily copied on a SD card and putted in the Raspberry PI. No need for complicate installation or configuration.

## Slide 3
ARISS webcast platform
AF-HD USB Webcam
Modem / Router
Raspberry Pi Interface
Audio IN
Audio OUT

## Slide 4
ARISS webcast platform
Hardware needed:
Raspberry PI development board
  CPU to acquire signal from USB camera, audio from radio or phone patch. Realtime encoding to USTREAM (or equivalent) webcast service
  Based on Linux customized distribution
  Configuration via web-if
USB audio interface
  AUDIO IN from radio or phone patch
  AUDIO OUT for contact audio recording (i.e. on a PC)
  Automatic audio recording on local USB memory or SD card – UNDER DEVELOPMENT
USB HD webcam
  HD camera with autofocus features
  Possible multiple camera control (meeting room, antenna, …) – UNDER DEVELOPMENT

## Slide 5
USTREAM.com webcast service
How it works?
Ustream.com support, through a dedicated API, embedding live transmission using an external software (i.e. VLC – videolan.org)

## Slide 6
HAM-TV
The same hardware could be easily configured to receive the HAM-TV streaming from the telebridge network. Raspberry PI has a video output (HDMI or Composite) to display/beamer.
HAM-TV streaming from chaining telebridge network
Audio OUT

## Slide 7
Questions
or
suggestions